## Slide 1: Configure STM32F3Discovery on Windows OS

## Slide 2: Tools
Rust 1.3.1 or later.
itmdump v0.3.1
OpenOCD >= v0.8
arm-none-eabi-gdb v7.12 or later
cargo-binutils v0.1.4 or later
PuTTY

## Slide 3: Installation (Rust & Cargo)
Install rustc & cargo from https://rustup.rs/ and follow the on-screen instructions
To verify the installation, type below instruction on the command line:
  rustc -V
It should give you the following output
  rustc 1.31.0 (abe02cefd 2018-12-04)

## Slide 4: Installation (itmdump)
Install itmdump with the following command.
  cargo install itm --vers 0.3.1
To verify the installation, type below instruction on the command line:
  itmdump -V
It should give you the following output
  itmdump 0.3.1

## Slide 5: Installation (cargo-binutils)
First, we need to install LLVM component for Rust. Add the component with the following command:
  rustup component add llvm-tools-preview
Install cargo-binutils with the following command.
  cargo install cargo-binutils --vers 0.1.4
To verify the installation, type below instruction on the command line:
  cargo size -- -version
It should give you the following output
  LLVM (http://llvm.org/):
    LLVM version 8.0.0svn
    Optimized build.
    Default target: x86_64-unknown-linux-gnu
    Host CPU: skylake

## Slide 6: Installation (arm-none-eabi-gdb)
Download it from the following location:
  https://github.com/ilg-archived/arm-none-eabi-gcc/releases/download/v8.2.1-1.7/gnu-mcu-eclipse-arm-none-eabi-gcc-8.2.1-1.7-20190524-0603-win64.zip
Unzip the folder at below location:
  C:\Users\<UserName>\AppData\Roaming
Update your %PATH% environment variable to include this path.
  C:\Users\<UserName>\AppData\Roaming\GNU Tools ARM Embedded\bin (verify that the path exists)
Check the installation with the following command:
  arm-none-eabi-gcc -v

## Slide 7: Installation (OpenOCD)
Download OpenOCD from the following location:
  https://github.com/ilg-archived/openocd/releases/download/v0.10.0-12-20190422/gnu-mcu-eclipse-openocd-0.10.0-12-20190422-2015-win64.zip
Unzip the folder at below location:
  C:\OpenOCD
Update your %PATH% environment variable to include the following path.
  C:\OpenOCD\bin (verify that the path exists)
Verify that OpenOCD is in your %PATH% with:
  openocd -v

## Slide 8: Installation (PuTTY)
Download PuTTY from the following location:
  https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html

## Slide 9: Installation (USB Driver)
Download ST-LINK USB Driver from the following location:
  https://www.st.com/en/development-tools/stsw-link009.html

## Slide 10: Verify the Installation

## Slide 11: Verify the Installation (contd.)